FAST FORTH V2.0 RESUMED

Words in parentheses () are the default execution of their paired word without parentheses that are DEFERed words.
Example of use: see words START and STOP in \MSP430-FORTH\RC5toLCD.f

Words in braces {} are MARKER words.

FORTH vocabulary
Words with hyperlink are ANSI compliant. The others are detailed below.

ASM CODE HI2LO COLD WARM (WARM) WIPE RST_HERE
PWR_HERE RST_STATE PWR_STATE MOVE LEAVE +LOOP LOOP DO
REPEAT WHILE AGAIN UNTIL BEGIN THEN ELSE IF
DEFER DOES> CREATE CONSTANT VARIABLE : ; POSTPONE
RECURSE IMMEDIATE IS ['] ] [ \ '
ABORT" ABORT QUIT EVALUATE COUNT LITERAL , EXECUTE
>NUMBER FIND WORD ." S" TYPE SPACES SPACE
CR (CR) NOECHO ECHO EMIT (EMIT) (ACCEPT) ACCEPT
KEY (KEY) C, ALLOT HERE . D. U.
SIGN HOLD #> #S # UM/MOD <# BL STATE BASE CIB J I UNLOOP U< > < = 0> 0< 0= DABS 1- 1+ ABS NEGATE - + C! C@ ! @ DEPTH R@ R> >R ROT OVER SWAP NIP DROP ?DUP DUP LIT EXIT

ASM <word> creates an assembler word as CODE but which is not interpretable by FORTH (because use of CALL ... RET).
        this defined <word> must be ended with ENDASM.
HI2LO used to switch from a high level (FORTH) to low level (assembler) modes.
COLD Software reset
WARM DEFERed word, initially executes (WARM)
(WARM) performs a hot start
WIPE resets the program memory to its original state.
RST_HERE defines the boundary of the program memory protected against COLD or hardware reset.
PWR_HERE defines the boundary of the program memory protected against ON/OFF and against any error occurring.
RST_STATE remove all words defined after RST_HERE
PWR_STATE remove all words defined after PWR_HERE
(CR)	executes ANS definition CR
(EMIT)	executes ANS definition EMIT
(ACCEPT)	executes ANS definition ACCEPT
(KEY)	executes ANS definition KEY
NOECHO stop display on output
ECHO start display on output
CIB	leave addr of Current Input Buffer
LIT execution part of LITERAL

ASSEMBLER vocabulary

?GOTO GOTO FW3 FW2 FW1 BW3 BW2 BW1
?JMP JMP REPEAT WHILE AGAIN UNTIL ELSE THEN
IF 0= 0<> U>= U< 0< 0>= S<
S>= RRUM RLAM RRAM RRCM POPM PUSHM CALL
PUSH.B PUSH SXT RRA.B RRA SWPB RRC.B RRC
AND.B AND XOR.B XOR BIS.B BIS BIC.B BIC
BIT.B BIT DADD.B DADD CMP.B CMP SUB.B SUB
SUBC.B SUBC ADDC.B ADDC ADD.B ADD MOV.B MOV
RETI LO2HI COLON ENDASM ENDCODE (SLEEP) SLEEP

?GOTO used after a conditionnal (0=,0<>,U>=,U<,0<,S<,S>=) to branch to a label FWx or BWx
GOTO used as unconditionnal branch to a label FWx or BWx

FW3 FORWARD branch destination n°3
FW2 FORWARD branch destination n°2
FW1 FORWARD branch destination n°1

BW3 BACKWARD branch destination n°3
BW2 BACKWARD branch destination n°2
BW1 BACKWARD branch destination n°1

?JMP used after a conditionnal (0=,0<>,U>=,U<,0<,S<,S>=) to jump to a defined word
JMP unconditionnal jump to a defined word

REPEAT assembler version of the FORTH word REPEAT (unconditionnal branch)
WHILE assembler version of the FORTH word WHILE (conditionnal branch preceded by 0=,0<>,U>=,U<,0>=,S<,S>=)
AGAIN assembler version of the FORTH word AGAIN (unconditionnal branch)
UNTIL assembler version of the FORTH word UNTIL (conditionnal branch preceded by 0=,0<>,U>=,U<,0>=,S<,S>=)
ELSE assembler version of the FORTH word ELSE (unconditionnal branch)
THEN assembler version of the FORTH word THEN ends IF or IF ELSE statements
IF assembler version of the FORTH word IF (conditionnal branch preceded by 0=,0<>,U>=,U<,0>=,S<,S>=)

LO2HI switches between low level and high level interpretation mode (counterpart of HI2LO), without saving IP.
COLON pushes IP then performs LO2HI, used as: CODE <word> ... assembly code ... COLON ... FORTH words ... ;
ENDASM to end an ASM definition
ENDCODE to end a CODE definition
(SLEEP) performs the default background task. See (ACCEPT) in ForthMSP430FRxxxx.asm
SLEEP DEFERed word, initially executes (SLEEP), and which enables you to create your own background task.

To better understand the use of the assembler I refer you to \MSP430-FORTH\ANS_COMP.f.

Here are adds-on to be compiled

CONDCOMP

[DEFINED] [UNDEFINED] [IF] [ELSE] [THEN] COMPARE MARKER

VOCABULARY

DEFINITIONS ONLY PREVIOUS ALSO ASSEMBLER FORTH VOCABULARY

FORTH	replace first words set in CONTEXT by the words set FORTH
ASSEMBLER	replace first words set in CONTEXT by the words set ASSEMBLER
VOCABULARY	VOCABULARY TRUC creates a new words set called TRUC

SD_CARD_LOADER

LOAD"

LOAD" LOAD" SD_TEST.4TH" loads file SD_TEST.4TH to FASTFORTH.

SD_CARD_READ_WRITE

TERM2SD" SD_EMIT WRITE READ CLOSE DEL" WRITE" READ"

TERM2SD" TERM2SD" SD_TEST.4TH" copy input file to SD_CARD (use CopySourceFileToTarget_SD_Card.bat to do)
SD_EMIT sends output stream at the end of last opened as write file.
WRITE write sequentially BUFFER content to a sector
READ read sequentially a sector to BUFFER
CLOSE close last opened file.
DEL" DEL" SD_TEST.4TH" remove this file from SD_CARD.
WRITE" WRITE" TRUC" open or create TRUC file ready to write to the end of this file
READ" READ" TRUC" open TRUC and load its first sector in BUFFER

see SD_TEST.f

Below, adds-on that can be compiled in kernel or loaded later

FIXPOINT

2CONSTANT D>F S>F F. F* F#S F/ F- F+ HOLDS {FIXPOINT}

ANS_COMPLEMENT

PAD	>IN >BODY SOURCE .( ( DECIMAL HEX FILL [CHAR] CHAR +! 2/ 2* MIN MAX RSHIFT LSHIFT INVERT 2OVER 2SWAP 2DROP 2DUP 2! 2@ S>D CELL+ CELLS CHAR+ CHARS ALIGN ALIGNED */ */MOD MOD / /MOD * FM/MOD SM/REM M* UM* XOR OR AND {ANS_COMP}

UTILITY

DUMP U.R WORDS ? .RS .S {UTILITY}

U.R u z -- display unsigned number u with size z
.RS display Return Stack content
{UTILITY} if you type {UTILITY} all subsequent loaded words are removed

SD_TOOLS

DIR FAT CLUSTER SECTOR {SD_TOOLS}

DIR dump first sector of current directory
FAT dump first sector of FAT1
CLUSTER .123 CLUSTER displays first sector of cluster 123
SECTOR .123456789 SECTOR displays sector 123456789
{SD_TOOLS} if you type {SD_TOOLS} all subsequent loaded words are removed

build your FastForth local copy

download https://github.com/jean-michel/FAST-FORTH/archive/master.zip
once you have unzipped it into your folder, share it (with you) and notice its network path.
Then right clic on the root of your notepad to create a network drive by recopying this network path (change backslashes \ to slashes / ); then set drive letter as you want.

In explorer you should obtain that:

drive:\prog\	TERATERM.ini
drive:\prog\gema\
drive:\prog\MacroAssemblerAS\bin\
drive:\prog\MSP430Flasher\
drive:\prog\Srecord\
drive:\prog\wscite\	SciTEGlobal.properties

drive:\	source files to build FASTFORTH, including files for KERNEL ADD-ON switches
drive:\ADD-ON\	FASTFORTH build ADD-ON files for OPTIONAL KERNEL ADD-ON switches (not erasable version)
drive:\MSP430-FORTH\	FORTH source files
drive:\config\gema\	GEMA pattern files
drive:\config\msp430\	bat files
drive:\config\scite\	others.properties
hex.properties
drive:\config\scite\AS_MSP430\	SCITE configuration files

source files to build FASTFORTH, including files for KERNEL ADD-ON switches:
drive:\ForthMSP430FRxxxx.asm	main FASTFORTH program
      \ForthMSP430FRxxxx_ASM.asm	assembler
      \ForthMSP430FRxxxx_SD_ACCEPT.asm	ACCEPT from SD_CARD
      \ForthMSP430FRxxxx_SD_INIT.asm	to init SD_CARD (FAT16/32)
      \ForthMSP430FRxxxx_SD_LOAD.asm	to load source files from SD_CARD
      \ForthMSP430FRxxxx_SD_LowLevel.asm	SPI routines + Read / write sector
      \ForthMSP430FRxxxx_SD_RW.asm	to read create write del SD_CARD files + file copy from terminal to SD_CARD
      \prog.bat 'drag and drop' programing bat file (hard link)
      \*.inc files	targets configuration files
      \*.asm files targets (minimalist) init files
      \*.mac files	macros files for AS assembler
      \*.txt files program files ready to 'drag and drop' onto prog.bat
      \SciTEDirectories.properties copy of \config\scite\AS_MSP430\SciTEDirectories.properties

FASTFORTH build ADD-ON files for OPTIONAL KERNEL ADD-ON switches (not erasable option version): drive:\ADD_ON\ALIGNMENT.asm
ANS_COMPLEMENT.asm
ARITHMETIC.asm
CONDCOMP.asm
DOUBLE.asm
PORTABILITY.asm
SD_TOOLS.asm
UTILITY.asm

FORTH source files:
drive:\MSP430-FORTH\*.4th	pure FORTH generic source files ready to download without preprocessing
   *.f	source files with use of assembler, must be preprocessed before downloading
   *.bat	to download source file to target, to SD_CARD target, and to debug (hard links)
        ANS_COMP.f	same as ANS_COMP.asm, (erasable)
   SD_TOOLS.f	same as SD_TOOLS.asm, (erasable)
   UTILITY.f	same as UTILITY.asm, (erasable)
   RTC.f	to set time and date with embedded RTC
   BOOT.f	performs bootstrap
   RC5toLCD.f	multitasking example:
        SD_test.f	tests for SD_CARD option: contains the explanations

drive:\MSP430-FORTH\MISC\ empty directory. See use in SD_TEST.f

GEMA pattern files
drive:\config\gema\FastForthREGtoTI.pat converts FORTH symbolic registers names to TI Rx registers
      \config\gema\MSP430FR2x4x.pat declarations for MSP430FR2 MSP430FR4 families, assembly part
      \config\gema\MSP430FR2x4x_FastForth.pat declarations for MSP430FR2 MSP430FR4 families, FORTH part
      \config\gema\MSP430FR5x6x.pat declarations for MSP430FR6 MSP430FR6 families, assembly part
      \config\gema\MSP430FR5x6x_FastForth.pat declarations for MSP430FR5 MSP430FR6 families, FORTH part
      \config\gema\MSP430FR57xx.pat declarations for MSP430FR57 family, assembly part
      \config\gema\MSP430FR57xx_FastForth.pat declarations for MSP430FR57 family, FORTH part
      \config\gema\MSP430FRxxxx.pat assembly declarations for device MSP430FRxxxx
      \config\gema\RemoveComments.pat
      \config\gema\SciTEDirectory.properties copy of \config\scite\AS_MSP430\SciTEDirectories.properties
      \config\gema\tiREGtoFastForth.pat converts TI Rx registers to FORTH symbolic registers names
      \config\gema\target.pat	declarations for target
      \config\gema\launchpad_x.pat	assembly declarations for specific target

SCITE configuration files:
drive:\config\scite\AS_MSP430\SciTEDirectories.properties	scite directory config file
        asm.properties	configuration for *.inc,*.mac,*.asm files
        forth.properties	configuration for *.f,*.4th files
    fortran.properties	configuration for *.pat files

drive:\config\msp430\SendFile.ttl	TERATERM macro file to send source file to FASTFORTH
        SendToSD.ttl	TERATERM macro file to send source file to embedded SD_CARD
        build(.bat)	called by scite to build target.txt program
        prog(.bat)	to flash target with target.txt file
        CopyTo_SD_Card(.bat)	to copy in your MSP430-FORTH
        SendSource(.bat)	to send file to FASTFORTH
        Preprocess(.bat)	to convert generic .f file to specific .4th file
        CopySourceFileToTarget_SD_Card.bat	to copy in any user folder for drag'n drop use
        SendSourceFileToTarget.bat	to copy in any user folder for drag'n drop use
        PreprocessSourceFile.bat	to copy in any user folder for drag'n drop use
   SelectTarget.bat	called by them three to select target

Note: all actions made from SciTE editor are processed via bat/bash files.
      So you can easily use your prefered editor by reuse them.

Note: all actions (flashing target, downloading files) can be made by using bat files directly, i.e. without use of SciTE	editor.
The next is to download IDE (WINDOWS):

First get TI's programs

go here: http://www.ti.com/ and registers you to enable MSP430Flasher downloading:

http://www.ti.com/tool/msp430-flasher?DCMP=MSP430&HQS=Other+OT+msp430flasher
and
http://software-dl.ti.com/msp430/msp430_public_sw/mcu/msp430/MSP430_FET_Drivers/latest/index_FDS.html

install in the suggested directory,
then copy MSP430Flasher.exe and MSP430.dll to drive:\prog\MSP430Flasher\

download and install teraterm: http://logmett.com/tera-term-the-latest-version

https://sourceforge.net/projects/gema/files/latest/download
unzip in drive:\prog\gema\

download http://www.scintilla.org/Sc400.exe to drive:\prog\wscite\
then rename Sc400.exe to scite.exe

http://john.ccac.rwth-aachen.de:8000/ftp/as/precompiled/i386-unknown-win32/aswcurr.zip
unzip in drive:\prog\MacroAssemblerAS\

https://sourceforge.net/projects/srecord/files/latest/download
unzip in drive:\prog\Srecord\

In explorer you should obtain that (minimum requested programs):

drive:\prog\	TERATERM.ini

drive:\prog\gema\	gema.exe	syntactic preprocessor

drive:\prog\MacroAssemblerAS\bin\	asw.exe	macro assembler
P2hex.exe	linker
as.msg
cmdarg.msg
ioerrs.msg
P2hex.msg
tools.msg

drive:\prog\MSP430Flasher\	MSP430Flasher.exe	flasher
MSP430.dll

drive:\prog\Srecord\	srec_cat.exe	TI.hex to TI.txt files converter

drive:\prog\wscite\	sCiTE.exe	text editor
SciTEGlobal.properties

Next we need to change the drive letter in hard links below:

drive:\prog.bat

drive:\MSP430-FORTH\SendSourceFileToTarget.bat
   CopySourceFileToTarget_SD_Card.bat
   PreprocessSourceFile.bat

to do, right clic on them
select "properties"
set your drive letter in "target"

The last step is ask Windows to associate scite editor with file types:

right clic on a .asm file,
select "open with",
select "other application" then select: drive:\prog\wscite\scite.exe

repeat for .inc, .mac, .lst, .f, .4th, .pat, .properties, .TTL files.

IT's done ! See forthMSP430FRxxxx.asm to configure TeraTerm

IDE for linux UBUNTU / MINT

First search from ti.com:

http://software-dl.ti.com/msp430/msp430_public_sw/mcu/msp430/MSP430Flasher/latest/index_FDS.html

untar in a home folder then:
open MSPFlasher-1.3.16-linux-x64-installer.run
    install in MSP430Flasher (under home)

open a terminal in MSP430Flasher/Drivers:
    sudo ./msp430uif_install.sh

copy MSP430Flasher/MSP430Flasher to /usr/local/bin/MSP430Flasher
copy MSP430Flasher/libmsp430.so to /usr/local/lib/MSP430Flasher/libmsp430.so

open an editor as superuser in /etc/ld.so.conf.d/
     write on first line (of new file): /usr/local/lib/msp430flasher/
     save this new file as libmsp430.conf
then in a terminal: sudo /sbin/ldconfig

install the package srecord

install the package scite
as super user, edit /etc/scite/SciTEGlobal.properties
uncomment (line 18): position.maximize=1
uncomment (line 257): properties.directory.enable=1
add line 7: PLAT_WIN=0
add line 8: PLAT_GTK=1
save file

at the end of your ~.profile file, add these two lines:
FF="/the_root_of_your_FastForth_local_copy"
export FF

https://sourceforge.net/projects/gema/files/gema/gema-1.4-RC/gema-1.4RC-src.tgz/download
untar in a home folder then:
make (ignore warnings)
sudo make install (ignore warnings)
make clean
result: /usr/local/bin/gema

http://john.ccac.rwth-aachen.de:8000/ftp/as/source/c_version/asl-current.tar.gz
untar in a home folder then:
copy /Makefile.def-samples/Makefile.def-i386-unknown-linux2.x,x to ../Makefile.def
edit this Makefile.def to remove "-march=i586" option from line 7
make
make test
sudo make install
make clean
result: asl files are in /usr/local

Here, you can compile FastForth from scite editor, so to generate file.4th

but... lack of TERATERM for linux !!!